## Slide 1: Rate-compatible Polar Coding and HARQ
11-11-2017

## Slide 2: Rate compatible polar codes
{C1,C2...CN} be a compound channel with R1>R2>R3...>RN, and block lengths n1<n2...<nN
Then the set is rate compatible if codeword for Ci can be built by removing nj-ni bits from codewords of code Cj ,j>i
Can be constructed by puncturing low rate codes.
Polar codes for degraded channels is inherently RCP

## Slide 3: HARQ =ARQ+FEC
Type –I
Send MSG+ED+EC
If recoverable with EC do so.
Else use ED to detect error and Retransmit
Use Chase combining
( like MRC) to decode finally
Effective SNRs for each Tx add.
Type –II
Send MSG+ED
if decodable do so.
Else Send EC incrementally
Decode using all the previous information.
Repeat from 3 if not decodable
Incremental Redundancy
Data sent on step 3 is RV or redundancy vector, can be chosen appropriately
Coding Gain obtained
HARQ for polar codes need a RCP and a HARQ scheme

## Slide 4: Scheme 1 (Kai chen)
M (polar bits ) | N-M repetition bits
K information bits | Chosen from the K bits
K information (msg) bits to be sent
RCP
Use N0 (block length of a low rate polar code)
Puncture to create N1<N2<N3...<NT<N0
T is the maximum number of repeats
RCP Block (K<=M<=N):

## Slide 5: Scheme 1 (Kai chen)
HARQ
A Type II ARQ (IR)
First Transmission N1 polar bits are sent
2nd onwards till ‘T’th transmission Nt-Nt-1 repetitions bits are sent.(Nt,K,M) RCPs constructed on each iteration.
i.e, The RVs are repetition bits chosen as follows
Selection of repetition bits
Choose the most error prone channel among the K bits,repeat this bit.
Step 1 increases the reliability , which is re- calculated.
Repeat from step 1.

## Slide 6: Scheme 2 (Kai chen , Incremental freezing)
A improvement over the previous scheme.
Uses reliability ordering to create puncturing patterns, thus the RCP.
Applicable to degraded channels only.
RV is repetition bits, choice of repetition bits is based on reliability ordering.
Extended to general channels by Mondelli , Hassani, using universal polarization (scheme 2a)
We have implemented this.

## Slide 7: Scheme 3(Tavildar)
RCP
Uses Subset Polar codes as RCP
Subset Polar code
Start with (N,K) polar code mother code
Create (M,K) subset code by puncturing, N>M, as follows:
  Fix a BLER
  puncture 1 bit
  estimate BLER
  change rate to get fixed BLER
  repeat from step 1 till (M,K) reached

## Slide 8: Scheme 3(Tavildar)
HARQ
Uses Uses Equivalent subset polar code as RV.
Equivalent subset Polar codes
Let S = {s1, s2, ..., sM} and T ={t1, t2, ..., tM}
be two (N M, K) subset polar codes. We say S is equivalent to T if si = ti ⊕ x ∀ i, 1 ≤ i ≤ M for some integer x, where 1 ≤ x ≤ N
cont...

## Slide 9: Scheme 3(Tavildar)
Equivalent subset polar codes create redundancy as:
If S, T are equivalent subset polar codes, then
channels W(i)N,S and W(i)N,T are equivalent for each 1 ≤ i ≤ N.
Where , bit channel equivalence is defined as follows:
Let W1 and W2 be two binary input channels
with output alphabets Y1 and Y2 respectively. We define the
two channels are equivalent, W1 ∼ W2, if there exists an
invertible function f : Y1 → Y2 such that W1(y1|x) =
W2(f(y1)|x).
Simulations suggest this beats previous schemes in terms of reliability under joint decoding.

## Slide 10: Use of CRC(DLC layer artefact) as ED
CRC is supposedly used or ED in all mentioned schemes.
Rateloss is negligible but not if short blocklengths are used.
Has other adverse effects like complexity due to cross layer cooperation.
Mukhtar et al. proposed CRC free HARQ with Turbo product codes using inherent ED capability of TPC.

## Slide 11: We are trying to get CRC-free HARQ with polar codes
Proposition 1:
If we can estimate the expected value of the abs(LLRs) of all the channels from some analytical expression(eg, Z) then ED is Binary Hypothesis testing between exactly 2 LLR vectors in each step.Further we can try ML decoding of this received LLR vector using some gaussian approximation of the LLR distribution(which looked like gaussian).
Proposition 2:
Errorchecking using frozen bits as mentioned here:
https://www.ncbi.nlm.nih.gov/pmc/articles/PMC4142331/